## Slide 1
Alternating currents, peak and RMS value of alternating current and voltage
CLASS-XII
SUBJECT : PHYSICS
CHAPTER NUMBER: 07
CHAPTER NAME : ALTERNATING CURRENT

## Slide 2
LEARNING OUTCOME
After this lesson, students will be able:
Explain from where electricity comes and how we use it.
Define electrical energy in terms of charge, voltage, current and resistance.
Identify the types of engineering careers that work primarily with electrical energy.

## Slide 3
Alternating emf:
Alternating emf is that emf which continuously changes in magnitude and periodically reverses its direction.
Alternating Current:
Alternating current is that current which continuously changes in magnitude and periodically reverses its direction.
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 sin ωt
I = I0 sin ωt
E, I – Instantaneous value of emf and current E0, I0 – Peak or maximum value or amplitude of emf and current
ω – Angular frequency t – Instantaneous time
ωt – Phase
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
0
π
2π
3π
4π
π/2
3π/2
5π/2
7π/2
θ = ωt
E ,I
E0
I0
E = E0 cos ωt
I = I0 cos ωt
Symbol of AC Source

## Slide 4
Average or Mean Value of Alternating Current:
Average or Mean value of alternating current over half cycle is that steady current which will send the same amount of charge in a circuit in the time of half cycle as is sent by the given alternating current in the same circuit in the same time.
dq = I dt = I0 sin ωt dt
q = ∫ I0 sin ωt dt
0
T/2
q = 2 I0 / ω = 2 I0 T / 2π = I0 T / π
Mean Value of AC, Im = Iav = q / (T/2)
Im = Iav = 2 I0 / π = 0.637 I0 = 63.7 % I0
Average or Mean Value of Alternating emf:
Em = Eav = 2 E0 / π = 0.637 E0 = 63.7 % E0
Note: Average or Mean value of alternating current or emf is zero over a cycle as the + ve and – ve values get cancelled.

## Slide 5
Root Mean Square or Virtual or Effective Value of Alternating Current:
Root Mean Square (rms) value of alternating current is that steady current which would produce the same heat in a given resistance in a given time as is produced by the given alternating current in the same resistance in the same time.
dH = I2R dt = I02 R sin2 ωt dt
H = ∫ I02 R sin2 ωt dt
0
T
H = I02 RT / 2
If Iv be the virtual value of AC, then
Iv = Irms = Ieff = I0 / √2 = 0.707 I0 = 70.7 % I0
Root Mean Square or Virtual or Effective Value of Alternating emf:
Ev = Erms = Eeff = E0 / √2 = 0.707 E0 = 70.7 % E0
Note: 1. Root Mean Square value of alternating current or emf can be calculated over any period of the cycle since it is based on the heat energy produced.
2. Do not use the above formulae if the time interval under the consideration is less than one period.
(After integration, ω is replaced with 2 π / T)
H = Iv 2 RT

## Slide 6
0
π
2π
3π
4π
T/4 T/2 3T/4 T 5T/4 3T/2 7T/4 2T
t
π/2
3π/2
5π/2
7π/2
θ = ωt
E0
Ev
Em
Relative Values Peak, Virtual and Mean Values of Alternating emf:
Em = Eav = 0.637 E0
Ev = Erms = Eeff = 0.707 E0
Tips:
The given values of alternating emf and current are virtual values unless otherwise specified.
i.e. 230 V AC means Ev = Erms = Eeff = 230 V
AC Ammeter and AC Voltmeter read the rms values of alternating current and voltage respectively.
They are called as ‘hot wire meters’.
3. The scale of DC meters is linearly graduated where as the scale of AC meters is not evenly graduated because H α I2

## Slide 7
HOME ASSIGNMENT
Two bulbs are rated (If they are connected (i) in series and (ii) in parallel across a supply V, find the power dissipated in the two combinations in terms of and .
Two electric bulbs P and Q have their resistances in the ratio of 1:2. They are connected in series across a battery. Find the ratio of the power dissipation in these bulbs.
3. A 25 W and a 100W bulb are joined in (i) series (ii) parallel and connected to the main. Which bulb glows brighter?

## Slide 8
THANKING YOU
ODM EDUCATIONAL GROUP