## Slide 1
Power in AC circuits, Power factor Wattles current,
CLASS-XII
SUBJECT : PHYSICS
CHAPTER NUMBER: 07
CHAPTER NAME : ALTERNATING CURRENT

## Slide 2
LEARNING OUTCOME
After this lesson, students will be able:
Explain from where electricity comes and how we use it.
Define electrical energy in terms of charge, voltage, current and resistance.
Identify the types of engineering careers that work primarily with electrical energy.

## Slide 3
Power in AC Circuit with L, C, R:
Instantaneous Power = E I
= E0 I0 sin ωt sin (ωt + Φ)
= E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ]
E = E0 sin ωt
I = I0 sin (ωt + Φ) (where Φ is the phase angle between emf and current)
If the instantaneous power is assumed to be constant for an infinitesimally small time dt, then the work done is
dW = E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ]
Work done over a complete cycle is
W = ∫ E0 I0 [sin2 ωt cosΦ + sin ωt cosωt cosΦ] dt
0
T
W = E0I0 cos Φ x T / 2
Average Power over a cycle is Pav = W / T
Pav = (E0I0/ 2) cos Φ
Pav = (E0/√2) (I0/ √2) cos Φ
(where cos Φ = R / Z
= R /√ [R2 + (ω L – 1/ωC)2] is called Power Factor)
Pav = Ev Iv cos Φ

## Slide 4
Ev
Power in AC Circuit with R:
In R, current and emf are in phase.
Φ = 0°
Pav = Ev Iv cos Φ = Ev Iv cos 0° = Ev Iv
Power in AC Circuit with L:
In L, current lags behind emf by π/2.
Φ = - π/2
Pav = Ev Iv cos (-π/2) = Ev Iv (0) = 0
Power in AC Circuit with C:
In C, current leads emf by π/2.
Φ = + π/2
Pav = Ev Iv cos (π/2) = Ev Iv (0) = 0
Note:
Power (Energy) is not dissipated in Inductor and Capacitor and hence they find a lot of practical applications and in devices using alternating current.
Pav = Ev Iv cos Φ
Wattless Current or Idle Current:
Iv
Iv cos Φ
Iv sin Φ
Φ
90°
The component Iv cos Φ generates power with Ev.
However, the component Iv sin Φ does not contribute to power along Ev and hence power generated is zero. This component of current is called wattless or idle current.
P = Ev Iv sin Φ cos 90° = 0

## Slide 5
HOME ASSIGNMENT
Two bulbs are rated (If they are connected (i) in series and (ii) in parallel across a supply V, find the power dissipated in the two combinations in terms of and .
Two electric bulbs P and Q have their resistances in the ratio of 1:2. They are connected in series across a battery. Find the ratio of the power dissipation in these bulbs.
3. A 25 W and a 100W bulb are joined in (i) series (ii) parallel and connected to the main. Which bulb glows brighter?

## Slide 6
THANKING YOU
ODM EDUCATIONAL GROUP