## Slide 1
GUIDED MEDIA
PERIOD-3
SUBJECT: COMPUTER SCIENCE
CHAPTER NUMBER: 8
CHAPTER NAME: NETWORKING

## Slide 2
Learning Outcomes:
Students will learn about different cables
Learn about their pros and cones
And know about their types available

## Slide 3
Discussed So Far :
Elementary terminologies of networks
Switching technique
Data communication terminologies

## Slide 4
SUB-CONCEPTS:
Twisted pair cable
Coaxial cable
Optical fibre

## Slide 5
Twisted Pair Cable:
      The most common form of wiring in data communication application is the twisted pair cable.
      As a voice grade medium (VGM), it is the basis for most internal office telephone wiring.
      It consists of two identical wires wrapped together in a double helix.
      Problems can occur due to differences in the electrical characteristics between the pair (e.g., length, resistance, capacitance).
      For this reason, LAN applications will tend to use a higher quality cable known as data grade medium (DGM).

## Slide 6
      Different types and categories of twisted-pair cable exist, but they all have two things in common:​
          The wires come in pairs.​
          The pairs of wires are twisted around each other.​
​
      The twisting of wires reduces crosstalk, which is the bleeding of a signal from one wire to another and which can corrupt signal and cause network errors. ​
      The twisting of the wires not only protects the signal from internal crosstalk, but it also protects it form other external forms of signal interference is called crosstalk.​

## Slide 7
(ii) Unshielded twisted pair cable
insulators
Twisted pair cable
(iii) Shielded twisted pair cable

## Slide 8
Advantages:
      The main advantages of twisted pair cable are :
            It is simple.
            It is easy to install and maintain.
            It is physically flexible.
            It has a low weight.
            It can be easily connected.
            It is very inexpensive

## Slide 9
Disadvantages:
      Because of high attenuation, it is incapable of carrying a signal over long distances without the use of repeaters (discussed later in the chapter).​
      Its low bandwidth capabilities make it unsuitable for broadband applications.​
      It supports maximum data rates 1 Mbps without conditioning and 10 Mbps with conditioning.​

## Slide 10
Types Of Twisted Pair Cables:
      Unshielded Twisted Pair (UTP) Cable.
        UTP cabling is used for variety of electronic communications. The UTP cables can have maximum segment length of 100 metres.
      Shielded Twisted Pair (STP) Cable.
        This type of cables comes with shielding of the individual pairs of wires, which further protects it from external interference. But these also, like UTP, can have maximum segment length of 100 meters.
      The advantage of STP over UTP is that it offers greater protection from interference crosstalk due to shielding. But it is heavier and costlier than UTP and requires proper grounding at both ends.

## Slide 11
Coaxial Cable:
      This type of cable consists of a solid wire core surrounded by one or more foil or wire shields, each separated by plastic insulator.
      The inner core carries the signal, and the shield provides the ground.
      The coaxial cable has high electrical properties and is suitable for high speed communication.
      It is widely used for television signals. In the form of (CATV) cable, it provides a cheap means of transporting multi-channel television signals around metropolitan areas.
      It is also used by large corporations in building security systems.

## Slide 13
Advantages:
      The data transmission characteristics of coaxial cables are considerably better than those of twisted-pair cables.
      The coaxial cables can be used as the basis for a shared cable network.
      The coaxial cables can be used for broadband transmission i.e., several channels can be transmitted simultaneously (as with cable TV).
      Offers higher bandwidths-up to 400 MBPS.

## Slide 14
Disadvantages​:
      Expensive compared to twisted pair cables.​
      The coaxial cables are not compatible with twisted pair cables.
        ​
Types of Coaxial Cables:
      Thicknet. This form of coaxial cable is thicker than thinnet. The thicknet coaxial cable segments (while joining nodes of a network) can be up to 500 meters long.​
      Thinnet. This form of coaxial cable is thinner, and it can have maximum segment length of 185 meters i.e., using this cable, nodes having maximum distance of 185 meters can be joined.​

## Slide 15
Optical Fibres:
      Optical fibres consist of thin strands of glass or glass like material which are so constructed that they carry light from a source at one end of the fibre to a detector at the other end.
      The light sources used are either light emitting diodes (LEDs) or laser diodes (LDs).
      The data to be transmitted is modulated onto the light beam using frequency modulation techniques. The signals can then be picked up at the receiving end and demodulated.

## Slide 16
Core
Cladding
Sheath
The fibre cable consists of three pieces : ​
    The core: the glass or plastic through which the light travels ​
    The cladding: which is a covering of the core that reflects light back to the core​
    Sheath: a protective coating, which protects the fiber cable from hostile environment​

## Slide 17
Advantages:
      It is immune to electrical and magnetic interference i.e., noise in any form because the information is travelling on a modulated light beam.
      It is highly suitable for harsh industrial environments.
      it guarantees secure transmission and has an extremely high transmission capacity.
      Fiber optic cables can be used for broadband transmission where several channels (i.e., bands of frequency) are handled in parallel and where it is also possible to mix data transmission channels with channels for telescope, graphics, TV, and sound.

## Slide 18
Disadvantages​:
      Installation problem. Fiber optic cables are quite fragile and may need special care to make them sufficiently robust for an office environment.​
      Connecting either two fibers together or a light source to a fiber is a difficult process.​
      Because of noise immunity, optical fibers are virtually impossible to tap. To incept the signal, the fiber must be cut and a detector inserted.​
      Light can reach the receiver out of phase.​
      Connection losses are common problems.​
      Fiber optic cables are more difficult to solder.​
      They are the most expensive of all the cables.​

## Slide 19
Types of Fibre Optic Cables:
  Single node :
      That supports a segment length of up to 2 kms and band- width of up to 100 Mbps
  Multi node:
      With a segment length of 100 kms and bandwidth of 2 Gbps.

## Slide 20
SESSION REVIEW:
Twisted pair cable
Coaxial cable
Optical fibre

## Slide 21
ASSIGNMENT:
Write advantages of twisted pair cables.
Write the disadvantages of coaxial cable.
Write the advantages of optical fibre.

## Slide 22
THANKING YOU
ODM EDUCATIONAL GROUP