## Slide 1
UNGUIDED MEDIA
PERIOD-4
SUBJECT: COMPUTER SCIENCE
CHAPTER NUMBER: 8
CHAPTER NAME: NETWORKING

## Slide 2
Learning Outcomes:
Students will learn about unguided media.
Know their pros and cones
Learn about different types of networks

## Slide 3
Discussed So Far :
Twisted pair cable
Coaxial cable
Optical fibre

## Slide 4
SUB-CONCEPTS:
Different unguided media
Their pros and cones
Types of Network

## Slide 5
Unguided Media:
  Microwave (Terrestrial Microwave):
      Microwave signals are used to transmit data without the use of cables.
      They are like radio and television signals and are used for long distance communication.
      The microwave transmission consists of a transmitter, receiver, and the atmosphere.
      In microwave communication, parabolic antennas are mounted on towers to send a beam to other antennas tens of kilometres away.
      The higher the tower, the greater the range.
      With a 100-meter high tower, distances of 100 km between towers are feasible.
      The microwave transmission is line-of-sight1 transmission.

## Slide 6
Advantages:
      It proves cheaper than digging trenches for laying cables and maintaining repeaters and cables if cables get broken by a variety of causes.
      It offers freedom from land acquisition rights that are required for laying, repairing the cables.
      It offers ease of communication over difficult terrain.
      Microwaves can communicate over oceans.

## Slide 7
Disadvantages​:
      Microwave communication is an insecure communication.​
      Signals from a single antenna may split up and propagate by slightly different paths to the receiving antenna. When these out-of-phase signals recombine, they interfere, reducing the signal strength.​
      Microwave propagation is susceptible to weather effects like rains, thunder storms etc.​
      Bandwidth allocation is extremely limited in case of microwaves.​
      The cost of design, implementation, and maintenance of microwave links is high.​

## Slide 8
Satellite (Satellite Microwave):
      Satellite communication is special case of microwave relay system.
      Satellite communications use the synchronous satellite to relay the radio signal transmitted from ground station.
      It provides voice, fax, data, and video services as well as email, file transfer, WWW internet applications.
      When fixed wire terrestrial communication networks are crushed by a disaster, the satellite and microwave system as an emergency backup facility will be stressed.
      The security in satellite transmission is usually provided by the coding and decoding equipment.

## Slide 9
In satellite communication the earth station consists of a satellite dish that functions as an antenna and communication equipment to transmit and receive data from satellites passing overhead.​
Several communication satellites, owned by both governments and private organizations, have been placed in stationary orbits about 22,300 miles above the earth’s surface. ​
These satellites act as relay stations for communication signals. The satellites accept data/ signals transmitted from an earth station, amplify them, and retransmit them to another earth station. Using such a setup, data can be transmitted to the other side of the earth in only one step.​
Most communication satellites have multiple, independent reception and transmission devices known as transponders.​

## Slide 10
Advantages:
      Radio-wave transmission offers mobility.
      It proves cheaper than digging trenches for laying cables and maintaining repeaters and cables if cables get broken by a variety of causes.
      It offers freedom from land acquisition rights that are required for laying, repairing the cables.
      It offers ease of communication over difficult terrain.
Disadvantages:
      Radio-wave communication is an insecure communication.
      Radio-wave propagation is susceptible to weather effects like rains, thunderstorms etc.

## Slide 11
Radio Wave:
        The transmission making use of radio frequencies is termed as radio-wave transmission.
        We all are familiar with radios and their working.
        When certain radio frequencies are allocated to private businesses for direct voice communication, they can make use of it for private business purposes.
        In general, private citizens and business users are licensed to operate in the range of about 10 miles.
        All radios today, however, use continuous sine waves to transmit information (audio, video, data).

## Slide 12
Each different radio signal uses a different sine wave frequency, and that is how they are all separated. Any radio setup has two parts :​
        1. The transmitter 2. The receiver​
The transmitter takes some sort of message (it could be the sound of someone’s voice, pictures for a TV set, data for a radio modem or whatever), encodes it onto a sine wave and transmits it with radio waves.​
The receiver receives the radio waves and decodes the message from the sine wave it receives.​
Both the transmitter and receiver use antennas to radiate and capture the radio signal.​

## Slide 13
Advantages:
      The area coverage through satellite transmission is quite large.
      The laying and maintenance of intercontinental cable is difficult and expensive, and this is where the satellite proves to be the best alternative.
      The heavy usage of intercontinental traffic makes the satellite commercial attractive.
      Satellites can cover large areas of the Earth. This is particularly useful for sparsely populated areas.

## Slide 14
Disadvantages​:
      Technological limitations preventing the deployment of large, high gain antennas on the satellite platform.​
      Over-crowding of available bandwidths due to low antenna gains.​
      The high investment cost and insurance cost associated with significant probability of failure.​
      High atmospheric losses above 30 GHz limit carrier frequencies.​

## Slide 15
Infrared:
      This type of transmission uses infrared light to send data.
      TV remotes, automotive garage doors, wireless speakers etc., all make use of infrared as transmission media.
      The infrared light transmits data through the air and can propagate throughout a room but will not penetrate walls.
      The infrared transmission has become common in PDAs (Personal digital assistants) e.g., handheld devices like palm pilots etc.
      The infrared transmission is a secure one.

## Slide 16
Laser:
      The laser transmission requires direct line-of-sight.
      It is unidirectional like microwave but has much higher speed than microwaves.
      The laser transmission requires the use of a laser transmitter and a photo-sensitive receiver at each end. The laser transmission is point-to-point transmission, typically between buildings.
      But lasers have a certain disadvantage, which is : it can be adversely affected by weather.

## Slide 17
Types Of Networks:
      A computer network means a group of computers that are linked by means of a communication system.
      A network can mean a small group of linked computers to a chain of a few hundred computers of different types (e.g., PCs, minis, mainframes etc.) spread around the world.
      Thus, networks vary in size, complexity, and geographical spread. Mostly, computers are classified based on geographical spread and on this basis, there can be four types of networks.

## Slide 18
Types:​
      Local Area Networks (LANs) ​
      Metropolitan Area Networks (MANs)​
      Wide Area Networks (WANs) ​
      Personal Area Network (PAN)​

## Slide 19
Local Area Networks (LANs):
      Small computer networks that are confined to a localised area (e.g., an office, a building, or a factory) are known as Local Area Networks (LANs).
      The key purpose of a LAN is to serve its users in resource sharing.
      The hardware as well as software resources are shared through LANs. For instance, LAN users can share data, information, programs, printer, hard-disks, modems etc.
      In a typical LAN configuration, one computer is designated as the file server.
      It stores all the software that controls the network, as well as the software that can be shared by the computers attached to the network.

## Slide 20
      Computers connected to the file server are called workstations. ​
      The work- stations can be less powerful than the file server, and they may have additional software on their hard drives. ​
      On most LANs, cables are used to connect the network interface cards in each computer.​

## Slide 21
Metropolitan Area Network (MAN):
      Metropolitan Area Networks are the networks spread over a city.
      For example, cable TV networks that are spread over a city, can be termed as metropolitan area networks.
      The purpose of a MAN is also the sharing of hardware and software resources among its users.

## Slide 22
Wide Area Networks (WAN)​:
      The networks spread across countries are known as WANs. ​
      A Wide Area Network (WAN) is a group of computers that are separated by large distances and tied together. ​
      It can even be a group of LANs that are spread across several locations and connected to look like one big LAN. ​
      The WANs link computers to facilitate fast and efficient exchange of information at lesser costs. ​
      Computers connected to a wide-area network are often connected through public networks, such as the telephone system.​
      Sometimes they can be connected through leased lines4 or satellites.​
      The largest WAN in existence is the Internet.​

## Slide 23
For example, a person traveling with a laptop, a personal digital assistant (PDA), and a portable printer could interconnect them without having to plug anything in, using some form of wireless technology such as Wi-Fi.
Typically, this kind of personal area network could also be interconnected without wires to the Internet or other networks.
You can use PAN networks to transfer files including email and calendar appointments, digital photos, and music etc from your portable devices such as phones and tablets to PC
A personal area network(PAN) is the interconnection of information technology devices within the range of an individual person, typically within range of 10 meters.
Personal Area Network(PAN):

## Slide 24
A Personal Area Network(PAN)

## Slide 25
Difference between a LAN and a WAN :
LAN | WAN
Diameter of not more than a few kilometers. A total data rate of at least several mbps. Complete ownership by a single organization. Very low error rates. | Span entire countries. Data rate less than 1 mbps. Owned by multiple organization. Comparatively higher error rates.

## Slide 26
SESSION REVIEW:
Different unguided media
Their pros and cones
Types of Network

## Slide 27
ASSIGNMENT:
What the different unguided media available.
Which of them is the best to use?
Write difference between LAN and WAN.

## Slide 28
THANKING YOU
ODM EDUCATIONAL GROUP