## Slide 1: ELECTRICITY
SUBJECT-PHYSICS CHAPTER NUMBER-8

## Slide 2: ELECTRICITY
https://youtu.be/CIv6vu9d73c
Electric Circuit: Electric circuit is a continuous and closed path of electric current.
Electric Current: The flow of electric charge is known as Electric Current, Electric current is carried by Moving electrons through a conductor.
By convention, electric current flows in the opposite direction to the movement of electrons.
If a net electric charge (Q) flows through a cross-section of a conductor in time t, then,
I = q/t.
Where I is electric current, Q is a net charge and t is a time in second.

## Slide 3: HOUSEHOLD ELECTRICITY
AC AND DC
The cell or battery provides us current which remains constant with time.This current is called DC.
The mains and electric generator provides us AC which changes its direction with time.
In India, we use AC of frequency 50 Hz.

## Slide 4: Electrical energy and power consumed in a circuit
Potential Difference: The work done in moving a unit positive charge from one point to another is known as potential difference.
W = QV
But I = Q/t
Q = It
W = Vit
Power is the rate of doing work.
P = Vit/t = VI.
SI unit of power = watt

## Slide 5: TRANSMISSION OF POWER FROM THE POWER GENERATING STATION TO THE CONSUMER
Generation of power
Power generating stations
Located very far, power = 11 kV, f= 50Hz
Raising of voltage
Voltage is raised from 11kV to 132 kV to reduce loss of energy
Transmitted to grid substations
Grid substation to main substation
At grid substation, voltage is reduced from 132 kV to 33 kV
At main substation, voltage is further reduced to 11 kV
At city substation, voltage is reduced to 220 V before it is supplied to consumer.

## Slide 6: Supply of power to a house
Supply electric power to house from city substation
Overhead wires or cables
Cable
Live or phase wire
Earth wire
Colour coding
Live: Red or brown : 220 V: To carry current from source to appliance
Neutral wire: Black or light blue: 0V: Provide return path from appliance to source
Neutral wire
Earth: Green or yellow: 0V: To provide connection to earth.

## Slide 7: THANKING YOU ODM EDUCATIONAL GROUP